| If oil was leaking from one of the high or low speed compression adjusters on a 6 Way Swinger, the adjusters should be replaced, Do Not remove unless a leak was detected. Remove the two 1.5mm set screws found on the backside of the reservoir forging. Remove the adjuster needles using a 3mm hex (Early Model Year 2004) or 2mm hex (Late Model Year 2004), Pour a small amount of damping oil in each hole prior to replacing the needles. | 1.5mm Set Screws Low Speed Needle (Red) High Speed Needle (Black) |
| --- | --- |
| Replace in reverse order. As you screw in the needles use a 2mm hex to guide the needle o-rings past the set screw openings to prevent damage. Apply blue locktite #242 to the set screws prior to installation. Tighten the set screw until it makes contact with the needle and then back off 1/4 turn. NOTE: Each adjuster needle is unique; replace one at a time to avoid confusion. |  |