2005 REAR SHOCK DAMPER BLEED - QUICK REFERENCE

These instructions apply after:

- All air pressure has been relieved from IFP and SVP reservoir/preloads

- Air volume adjuster removed from SPV, or reservoir cap from Metel RP.

- Damper is removed from the damper body - (Store submerged in oil)

- Rebound eyelet and rebound needle removed from damper shaft.

NON RESERVOIR SHOCKS

- Push IFP to bottom of damper body, relieving any backpressure in the preload chamber.

- Install the Schrader valve cap or IFP plug and stop screw.

- Set location of the damper shaft so that it extends past the damper cap as shown below.  For coil shocks, the shoulder (end) of the threads will be flush with the face of the damper cap.

| Shock | Shaft Extension |
| --- | --- |
| Air Shocks | 12.5mm |
| Coil Shocks | 8.5mm |

- Immerse damper body and damper in oil to bleed, tap to dislodge any air in the assy.

- Under oil, install air piston/damper onto the damper body hand tight.

- Remove from oil with damper shaft pointed up.

- Insert needle and needle o-ring at end of damper shaft.

- Tighten damper cap (Metel) or air piston (Radium & Swinger) to 150 KcCm

- Extend shaft; you can thread the eyelet on the shaft to assist.

- Clean damper shaft threads, install rebound eyelet using red Loctite. Torque to 120 KgCm.

RESERVOIR SHOCKS

- Install IFP in the reservoir body and set IFP to a depth of 25.8mm using 2005 IFP positioning tool.

- Set location of the damper shaft so that it extends past the damper cap as shown below.  For coil shocks, the shoulder (end) of the threads will be flush with the face of the damper cap.

| Shock | Shaft Extension |
| --- | --- |
| Air Shocks | 13.7mm |
| Coil Shocks | 8.5mm |

- End of shaft will be 8.5mm from damper cap face.

- Immerse damper body and damper in oil to bleed, tap to dislodge any air in the damper assembly.

- Install damper onto the damper body hand tight.

- Remove from oil with damper shaft pointed up.

- Insert needle into end of damper shaft.

- Tighter damper cap to 150 KgCm

- Clean damper shaft threads and install rebound eyelet using red Loctite.  Torque to 120 KgCm

FACTORY IFP/SPV PRESSURES

| Model | PSI |
| --- | --- |
| Radium & Radium R | 150/170 |
| Radium RL | 490/510 |
| Metel (All) | 160/180 |
| Swinger (All) | 120 |